## Slide 1
SMART INDIA HACKATHON 2026
@SIH Idea submission–Template
1
•Theme: Smart Automation •Category: Hardware •Team ID: SIH26-A0H-T341 •Team: Circuit Breakers
•Problem Statement ID: SIH26007
•Problem Statement Title: Safe and Efficient Operation
of Mine Vehicles in Fog and Low-Visibility Conditions in Open Cast Iron Ore Mines.

## Slide 2
PROPOSED SOLUTION
Circuit Breakers
@SIH Idea submission–Template
2
Problem at Hand
Reduced Visibility
Dense monsoon fog cuts sight distance to 3–5 m on Bailadila haul roads.
Delayed Hazard Detection
Operators spot obstacles and other ve- hicles too late to react safely.
Communication Gaps
Dumpers have no real-time link to warn each other or the control room.
Haul Road Congestion
Forced slowdowns and halts cut fleet productivity and ore evacuation.
Our Solution
Key Features
Adaptive: Continuously adjusts speed and alerts to real-time fog density—not fixed limits.
AI-Based Fog Navigation & Collision-Avoidance System
•Thermal & LiDAR Vision •Radar-Based Obstacle Detection •Visibility-Adaptive Speed Advisory •V2V/V2IHazardBroadcast
•Real-TimeFleetMonitoring •ModularRetrofitArchitecture
•DGPS Tracking
NMDC
AI-basedfognavi-
gation&collision- avoidancemodule
HAULDUMPER
•Fuses thermal camera, LiDAR and radar data
through a fusion engine.
•Detects obstacles and vehicles beyond human visual
range.
•Adjusts safe speed and following distance to real-
time visibility.
•Broadcasts vehicle position and hazards via
V2V/V2I links.
•Streams live fleet status to a digital-twin control
ro om.
Predictive:Flagscollisionriskandhazards beforetheyoccurusingsensorfusion.
Retrofit-Ready:Integrateswithexisting dumperfleetsviaCANbuswithoutredesign.

## Slide 3
TECHNICAL APPROACH
Circuit Breakers
@SIH Idea submission–Template
3
Hardware
Processing: STM32H7 + Raspberry Pi 5 (8GB)
Sensing: Thermal camera, LiDAR, mmWave radar, DGPS Actuation: HUD/display alerts, buzzer, LoRa/V2V radio, CAN interface
Software
Platform: ROS2 + Embedded C
Intelligence: Sensor Fusion + Kalman Filter
Sensor Fusion + Navigation: Multi-sensor fusion and adaptive speed control
ThermalImagingCamera
Thermalcamera—seesthroughfogviaheat signatures
mmWaveRadarSensor
Solid-stateLiDARarray
DGPS/IMUPositioning
DGPS+IMU—sub-metrepositionand heading
Fog Navigation & Collision-Avoidance Unit—STM32H7/Raspberry Pi 5 (8GB)
Sensor Fusion Estimator | V2V/V2I Communication Logic
10 Hz Cycle
01Thermal&LiDARPerception
Visibility-adaptivespeedadvisory +HUDalerts
02ObstacleDetection
Thermal+LiDAR+radarfusion forrangeandclassification →DelayedHazardDetection
03V2V/V2IAlertBroadcaster
Broadcastsposition,speedand hazardalertstonearbyvehicles
04FleetDashboard
Digital-twinfleetviewforthe controlroom →HaulRoadCongestion
→ReducedVisibility
→CommunicationGaps

## Slide 4
FEASIBILITY AND VIABILITY
Circuit Breakers
@SIH Idea submission–Template
4
Why it is feasible: The proposed system combines proven COTS sensors (thermal, LiDAR, radar, DGPS) with established sensor- fusion and V2V communication techniques.
Engineering Challenge
Fog and rain degrading camera and radar signal quality
GPS signal loss in hilltop/pit terrain
Rugged operation in dust and monsoon conditions; integration with fielded dumper fleets
Mitigation Strategy
Sensor fusion cross-validates thermal, LiDAR and radar readings; radar pen- etrates fog where optical sensors fail
DGPS with IMU dead-reckoning bridges GPS gaps
IP67 enclosures, vibration-rated mounts and a non-invasive CAN/V2V retrofit kit needing no dumper redesign

## Slide 5
IMPACT AND BENEFITS
Circuit Breakers
@SIH Idea submission–Template
Benefit Analysis
Target Audience & Impact Analysis
Ministry of Steel / National Steel Pol- icy
Supports the 100 MT by 2030 target
by protecting production continuity at Bailadila during the monsoon season.
Operational reliability
•Detects hazards before a collision oc-
curs
•Keeps haul cycle times stable across
visibility conditions
NMDC Haul Truck Operators
Safer driving in dense monsoon fog, fewer forced slowdowns or halts, and fewer near-miss incidents on haul roads.
NMDC Mine Management
A scalable system that sustains ore evacuation during monsoon fog while cutting accident-related downtime.
Cost & logistics savings
•Cuts production losses from fog-
related halts
•Reuses one retrofit kit across the en-
tire dumper fleet
Mission & safety impact
•Prevents collisions between dumpers in
dense fog
•Reduces haul-road accidents and near-
misses
•Gives operators real-time hazard visi-
bility
5

## Slide 6
RESEARCH AND REFERENCES
Circuit Breakers
@SIH Idea submission–Template
6
Technical Foundation & Prior Art
•DGMS Safety Circulars on HEMM Operation in Low-Visibility and Monsoon Conditions in Opencast Mines.
•Multi-Sensor Fusion (Thermal + LiDAR + Radar) for All-Weather Obstacle Detection in Autonomous Off-Road Vehicles
(IEEE Sensors Journal, 2023).
•V2V/V2I Communication Standards and Field Trials for Collision Avoidance in Mining and Off-Highway Vehicles (SAE
Technical Paper, 2024).
•NMDC Sustainability & Annual Reports—Bailadila Production Targets and Monsoon Operational Constraints.
•SIH 2026 Problem Statement SIH26007—Defines the Fog/Low-Visibility Challenge Context for NMDC Bailadila Haul
Roads.
•https://www.nmdc.co.in/—NMDC Limited, Production and Sustainability Reports